## Slide 1: White Rabbit Applications
John Gill, Dimitris Lampridis, Maciej Lipinski
CERN BE-CO
Hardware and Timing Section
BE-CO (virtual) Technical Meeting
14 May 2020

## Slide 2: Outline
Introduction to WR and overview of its applications
BTrain over WR (Maciej)
WR Trigger Distribution (Dimitris)
RF Signal Distribution over WR (John)
Q&A
2

## Slide 3: Outline
Introduction to WR and overview of its applications
BTrain over WR (Maciej)
WR Trigger Distribution (Dimitris)
RF Signal Distribution over WR (John)
Q&A
2

## Slide 4: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing

## Slide 5: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)

## Slide 6: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)

## Slide 7: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)

## Slide 8: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation
  Deterministic data transfer

## Slide 9: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation (included in IEEE 1588)
  Deterministic data transfer

## Slide 10: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation (included in IEEE 1588)
  Deterministic data transfer
Initial specs: links ≤10 km & ≤2000 nodes
<10km

## Slide 11: White Rabbit in a nutshell
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation (included in IEEE 1588)
  Deterministic data transfer
Initial specs: links ≤10 km & ≤2000 nodes
Many applications worldwide
3
Large High Altitude Air
Shower Observatory
German Stock Exchange
National Time Labs
(NL, FI, FR, US, UK, IT)
CERN & GSI
Accelerator Facilities
Cubic Kilometre
Neutrino Telescope
European Space Agency
for Galileo
Telecommunication for High Accuracy Time Dissemination
http://www.ohwr.org/projects/white-rabbit/wiki/WRUsers

## Slide 12: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation (included in IEEE 1588)
  Deterministic data transfer
Initial specs: links ≤10 km & ≤2000 nodes
Many applications worldwide
Open Source and commercially available

## Slide 13: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation (included in IEEE 1588)
  Deterministic data transfer
Initial specs: links ≤10 km & ≤2000 nodes
Many applications worldwide
Open Source and commercially available
More in “Introduction to WR Technologies” https://indico.cern.ch/event/862562/

## Slide 14: White Rabbit Applications
4
Time & frequency transfer
Time-based control
Precise timestamping
Trigger distribution (Dimitris)
Fixed-latency data transfer (Maciej)
Radio-frequency transfer (John)

## Slide 15: White Rabbit Applications
4
Time & frequency transfer
Time-based control
Precise timestamping
Trigger distribution (Dimitris)
Fixed-latency data transfer (Maciej)
Radio-frequency transfer (John)

## Slide 16: Time & frequency transfer
5
Widely used/evaluated by National Time Labs (5 countries)

## Slide 17: Time & frequency transfer
5
Widely used/evaluated by National Time Labs (5 countries)
ISPCS keynote Highly Accurate Time Dissemination & Network Synchronisation, Helmut Imlau, Deutsche Telekom

## Slide 18: White Rabbit Applications
Time & frequency transfer
Time-based control
Precise timestamping
Trigger distribution
Fixed-latency data transfer
Radio-frequency transfer

## Slide 19: Time-based control
6

## Slide 20: Time-based control
6

## Slide 21: Time-based control
6

## Slide 22: Time-based control
6

## Slide 23: Time-based control
7
GSI Heavy Ion Research in Germany
1-5 ns accuracy and 10 ps precision
WR network at GSI:
  Operational since June 2018:
  134 nodes & 32 switches
  Final: 2000 WR nodes & 300 switches in 5 layers

## Slide 24: White Rabbit Applications
Time & frequency transfer
Time-based control
Precise timestamping
Trigger distribution
Fixed-latency data transfer
Radio-frequency transfer

## Slide 25: Precise timestamping
8
Association of time with
  an event
  a sample (measured value)
The most widely used WR application
  Time-of-flight measurement
    Speed of neutrinos - CNGS
    Types of particles - ProtoDUNE
  Cosmic ray and neutrino detection
    Large High Altitude Air Shower Observatory
    Cubic Kilometre Neutrino Telescope
    Tunka Advanced Instrument for cosmic ray physics and Gamma Astronomy
  High Frequency Trade monitoring
    German Stock Exchange

## Slide 26: Precise timestamping
8
Association of time with
  an event
  a sample (measured value)
The most widely used WR application
  Time-of-flight measurement
    Speed of neutrinos - CNGS
    Types of particles - ProtoDUNE
  Cosmic ray and neutrino detection
    Large High Altitude Air Shower Observatory
    Cubic Kilometre Neutrino Telescope
    Tunka Advanced Instrument for cosmic ray physics and Gamma Astronomy
  High Frequency Trade monitoring
    German Stock Exchange

## Slide 27: Precise timestamping
8
Association of time with
  an event
  a sample (measured value)
The most widely used WR application
  Time-of-flight measurement
    Speed of neutrinos - CNGS
    Types of particles - ProtoDUNE
  Cosmic ray and neutrino detection
    Large High Altitude Air Shower Observatory
    Cubic Kilometre Neutrino Telescope
    Tunka Advanced Instrument for cosmic ray physics and Gamma Astronomy
  High Frequency Trade monitoring
    German Stock Exchange

## Slide 28: Precise timestamping
8
Association of time with
  an event
  a sample (measured value)
The most widely used WR application
  Time-of-flight measurement
    Speed of neutrinos - CNGS
    Types of particles - ProtoDUNE
  Cosmic ray and neutrino detection
    Large High Altitude Air Shower Observatory
    Cubic Kilometre Neutrino Telescope
    Tunka Advanced Instrument for cosmic ray physics and Gamma Astronomy
  High Frequency Trade monitoring
    German Stock Exchange

## Slide 29: Precise timestamping
8
Association of time with
  an event
  a sample (measured value)
The most widely used WR application
  Time-of-flight measurement
    Speed of neutrinos - CNGS
    Types of particles - ProtoDUNE
  Cosmic ray and neutrino detection
    Large High Altitude Air Shower Observatory
    Cubic Kilometre Neutrino Telescope
    Tunka Advanced Instrument for cosmic ray physics and Gamma Astronomy
  High Frequency Trade monitoring
    German Stock Exchange

## Slide 30: Precise timestamping
8
Association of time with
  an event
  a sample (measured value)
The most widely used WR application
  Time-of-flight measurement
    Speed of neutrinos - CNGS
    Types of particles - ProtoDUNE
  Cosmic ray and neutrino detection
    Large High Altitude Air Shower Observatory
    Cubic Kilometre Neutrino Telescope
    Tunka Advanced Instrument for cosmic ray physics and Gamma Astronomy
  High Frequency Trade monitoring
    German Stock Exchange

## Slide 31: Precise timestamping
8
Association of time with
  an event
  a sample (measured value)
The most widely used WR application
  Time-of-flight measurement
    Speed of neutrinos - CNGS
    Types of particles - ProtoDUNE
  Cosmic ray and neutrino detection
    Large High Altitude Air Shower Observatory
    Cubic Kilometre Neutrino Telescope
    Tunka Advanced Instrument for cosmic ray physics and Gamma Astronomy
  High Frequency Trade monitoring
    German Stock Exchange

## Slide 32: Precise timestamping
8
Association of time with
  an event
  a sample (measured value)
The most widely used WR application
  Time-of-flight measurement
    Speed of neutrinos - CNGS
    Types of particles - ProtoDUNE
  Cosmic ray and neutrino detection
    Large High Altitude Air Shower Observatory
    Cubic Kilometre Neutrino Telescope
    Tunka Advanced Instrument for cosmic ray physics and Gamma Astronomy
  High Frequency Trade monitoring
    German Stock Exchange

## Slide 33: Precise timestamping
8
Association of time with
  an event
  a sample (measured value)
The most widely used WR application
  Time-of-flight measurement
    Speed of neutrinos - CNGS
    Types of particles - ProtoDUNE
  Cosmic ray and neutrino detection
    Large High Altitude Air Shower Observatory
    Cubic Kilometre Neutrino Telescope
    Tunka Advanced Instrument for cosmic ray physics and Gamma Astronomy
  High Frequency Trade monitoring
    German Stock Exchange

## Slide 34: White Rabbit Applications
Time & frequency transfer
Time-based control
Precise timestamping
Trigger distribution
Fixed-latency data transfer
Radio-frequency transfer

## Slide 35: Trigger distribution
9

## Slide 36: Trigger distribution
9
LHC trigger distribution to measure beam instabilities - since 2016
WRTD - White Rabbit Trigger Distribution (next presentation) to be used for CERN’s Open Analog Signals Information System (OASIS)

## Slide 37: White Rabbit Applications
Time & frequency transfer
Time-based control
Precise timestamping
Trigger distribution
Fixed-latency data transfer
Radio-frequency transfer

## Slide 38: Fixed-latency data transfer
10

## Slide 39: Fixed-latency data transfer
10
Distribution of magnetic field in CERN accelerators (BTrain over WR, discussed later)
Distribution of RF signal for LLRF in SPS

## Slide 40: White Rabbit Applications
Time & frequency transfer
Time-based control
Precise timestamping
Trigger distribution
Fixed-latency data transfer
Radio-frequency transfer

## Slide 41: Radio-frequency transfer
11

## Slide 42: Radio-frequency transfer
11

## Slide 43: Radio-frequency transfer
12
RF over WR at European Synchrotron Radiation Facility (ESRF)
  A prototype tested in operation: <10 ps jitter
RF over WR at CERN (next presentation)
  A prototype: <100 fs jitter and <10 ps reproducibility over reboots

## Slide 44: Outline
WR in a nutshell and overview of its applications
BTrain over WR (Maciej)
WR Trigger Distribution (Dimitris)
RF Signal Distribution over WR (John)
Q&A

## Slide 45: Synchrotron operation
13
Beam Inst.
Diagnostics
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Coordination required between:
f (t) – RF in accelerating cavities
B(t) – magnetic field in bending magnets
I(t) – current provided by power converters
Beam Instrumentation diagnostics
I(t)

## Slide 46: Synchrotron operation
13
Beam Inst.
Diagnostics
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Coordination required between:
f (t) – RF in accelerating cavities
B(t) – magnetic field in bending magnets
I(t) – current provided by power converters
Beam Instrumentation diagnostics
Coordination provided by
the BTrain system
I(t)

## Slide 47: BTrain System
14
Beam Inst.
Diagnostics
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
I(t)

## Slide 48: BTrain System
14
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
B
B
B
Beam Inst.
Diagnostics
I(t)

## Slide 49: BTrain System
14
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
B
B
B
Beam Inst.
Diagnostics
I(t)
1us
24V
0.1 Gauss =
(max 500kHz)

## Slide 50: BTrain System
14
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Bflat top
time
B(t)
Bflat bottom
t1
t2
Peaking strip
marker 1
marker 2 (optional)
coil measurement Vcoil ~ Ḃ
B
B
B
Beam Inst.
Diagnostics
I(t)

## Slide 51: BTrain System
14
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Bflat top
time
B(t)
Bflat bottom
t1
t2
Peaking strip
marker 1
marker 2 (optional)
coil measurement Vcoil ~ Ḃ
+0.1G
- 0.1G
preset B(t1)
B(t)
B
B
B
Beam Inst.
Diagnostics
I(t)

## Slide 52: BTrain System
14
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Bflat top
time
B(t)
Bflat bottom
t1
t2
Peaking strip
marker 1
marker 2 (optional)
coil measurement Vcoil ~ Ḃ
+0.1G
- 0.1G
preset B(t1)
B(t)
B
B
B
Beam Inst.
Diagnostics
~ Vcoil
I(t)

## Slide 53: FIRESTORM to renovate BTrain
15
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Project by Magnets, Superconductors & Cryostats (TE-MSC) Group in collaboration with TE-EPC, BE-RF, BE-BI & BE-CO.
Why to renovate:
Higher resolution (0.05G) required in PS
Peak slope of 6T/s required by PSB
Spikes & noise on Bdot, timing problems with marker
Obsolete measurement technology and aging components
Non-standard equipment, little support from CO
Not uniform across accelerators & limited diagnostics
What to renovate:
Measurement technology – new markers and coils
Data transfer technology – White Rabbit
B
B
B
Beam Inst.
Diagnostics
I(t)

## Slide 54: FIRESTORM to renovate BTrain
15
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
Project by Magnets, Superconductors & Cryostats (TE-MSC) Group in collaboration with TE-EPC, BE-RF, BE-BI & BE-CO.
Why to renovate:
Higher resolution (0.05G) required in PS
Peak slope of 6T/s required by PSB
Spikes & noise on Bdot, timing problems with marker
Obsolete measurement technology and aging components
Non-standard equipment, little support from CO
Not uniform across accelerators & limited diagnostics
What to renovate:
Measurement technology – new markers and coils
Data transfer technology – White Rabbit
I(t)
WR Switch
WR Node

## Slide 55: BTrain data transfer over WR
16
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
WR Switch

## Slide 56: BTrain data transfer over WR
16
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
Digitally distributes absolute values of B and Bdot in Ethernet frames
Distributes simultaneously B from different sources (old B, measured B, simulated B, synthesized B)
Provides additional control information (C0, marker)
Supports resolution down to 0.0001G
Allows rates >500kHz and infinitely fast ramps
Deterministic & guarantees max latency of 10us
Provides extensive diagnostics
Provides flexibility and scalability
  I(t) is sent back for model analysis
CTRL | B | Bdot | oldB | meaB | simB | synB
WR Switch
CTRL
I
Payload of Ethernet Frame

## Slide 57: BTrain data transfer over WR
16
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
Digitally distributes absolute values of B and Bdot in Ethernet frames
Distributes simultaneously B from different sources (old B, measured B, simulated B, synthesized B)
Provides additional control information (C0, marker)
Supports resolution down to 0.0001G
Allows rates >500kHz and infinitely fast ramps
Deterministic & guarantees max latency of 10us
Provides extensive diagnostics
Provides flexibility and scalability
  I(t) is sent back for model analysis
  I(t) exchanged internally for Pole Face Winding (PFW) of Power Converters
CTRL | B | Bdot | oldB | meaB | simB | synB
WR Switch
CTRL
I
Payload of Ethernet Frame

## Slide 58: BTrain data transfer over WR
16
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
Digitally distributes absolute values of B and Bdot in Ethernet frames
Distributes simultaneously B from different sources (old B, measured B, simulated B, synthesized B)
Provides additional control information (C0, marker)
Supports resolution down to 0.0001G
Allows rates >500kHz and infinitely fast ramps
Deterministic & guarantees max latency of 10us
Provides extensive diagnostics
Provides flexibility and scalability
  I(t) is sent back for model analysis
  I(t) exchanged internally for Pole Face Winding (PFW) of Power Converters
CTRL | B | Bdot | oldB | meaB | simB | synB
WR Switch
CTRL
I
Payload of Ethernet Frame
SPS RF
  NOTE: Accelerating RF cavities to be
  controlled in SPS using WR

## Slide 59: WR-BTrain Nodes
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
WR Switch
17

## Slide 60: WR-BTrain Nodes
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
WR Switch
17
FPGA
FPGA
FPGA
Simple VME64x FMC Carrier (SVEC)
Simple PCIe FMC carrier (SPEC)
VME FMC Carrier HPC-DDR3 (VFC-HD)
VXS Switch
FPGA

## Slide 61: WR-BTrain Nodes
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
WR Switch
17
CO-supported
hardware
FPGA
FPGA
FPGA
FPGA
Simple VME64x FMC Carrier (SVEC)
Simple PCIe FMC carrier (SPEC)
VME FMC Carrier HPC-DDR3 (VFC-HD)
VXS Switch

## Slide 62: WR-BTrain Nodes
FPGA
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
Simple VME64x FMC Carrier (SVEC)
Simple PCIe FMC carrier (SPEC)
VME FMC Carrier HPC-DDR3 (VFC-HD)
VXS Switch
WR Switch
17
FPGA
FPGA
FPGA
CO-support
for
White Rabbit

## Slide 63: BTrain over White Rabbit Project
18
WR Switch
FPGA
BTrain over
White Rabbit
B
I
User logic
FPGA
BTrain over
White Rabbit
B
I
User logic
FPGA
BTrain over
White Rabbit
B
I
User logic
FPGA
BTrain over
White Rabbit
B
I
User logic
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home
FPGA
FPGA
FPGA
Simple VME64x FMC Carrier (SVEC)
Simple PCIe FMC carrier (SPEC)
VME FMC Carrier HPC-DDR3 (VFC-HD)
VXS Switch
FPGA

## Slide 64: BTrain over White Rabbit Project
WR Switch
18
FPGA
BTrain over
White Rabbit
B
I
User logic
FPGA
BTrain over
White Rabbit
B
I
User logic
FPGA
BTrain over
White Rabbit
B
I
User logic
FPGA
BTrain over
White Rabbit
B
I
User logic
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home

## Slide 65: BTrain over White Rabbit Project
WR Switch
18
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
FPGA
B
I
User logic
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network
WR Streamers
Data Transfer Layer: FIFO over White Rabbit
Statistics of network latency and lost frames
Option to fix latency at configurable value
BTrainFrameTransceiver
API to the user logic (VHDL records)
Encoding/decoding of BTrain Frames (format agreed by all BTrain users)
Transmission/reception of BTrain frames using WR Streamers
BTrainFrameTxRx
WR Streamers
WR PTP Core
BTrainFrameTxRx
WR Streamers
WR PTP Core
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home

## Slide 66: BTrain over White Rabbit Project
18
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network
WR Streamers
Data Transfer Layer: FIFO over White Rabbit
Statistics of network latency and lost frames
Option to fix latency at configurable value
BTrainFrameTransceiver
API to the user logic (VHDL records)
Encoding/decoding of BTrain Frames (format agreed by all BTrain users)
Transmission/reception of BTrain frames using WR Streamers
BTrainFrameTxRx
WR Streamers
WR PTP Core
WR Switch
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home

## Slide 67: BTrain over White Rabbit Project
WR Switch
18
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network

## Slide 68: BTrain over White Rabbit Project
18
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FIFO
FIFO
Latency
word
word
WR Switch
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network
WR Streamers
Data Transfer Layer: FIFO over White Rabbit
Statistics of network latency and lost frames
Option to fix latency at configurable value

## Slide 69: BTrain over White Rabbit Project
18
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FIFO
FIFO
Latency
word
word
WR Switch
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network
WR Streamers
Data Transfer Layer: FIFO over White Rabbit
Statistics of network latency and lost frames
Option to fix latency at configurable value

## Slide 70: BTrain over White Rabbit Project
18
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FIFO
FIFO
Latency
BFrame
IFrame
WR Switch
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network
WR Streamers
Data Transfer Layer: FIFO over White Rabbit
Statistics of network latency and lost frames
Option to fix latency at configurable value
BTrainFrameTransceiver
API to the user logic (VHDL records)
Encoding/decoding of BTrain Frames (format agreed by all BTrain users)
Transmission/reception of BTrain frames using WR Streamers

## Slide 71: BTrain over White Rabbit Project
18
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network
WR Streamers
Data Transfer Layer: FIFO over White Rabbit
Statistics of network latency and lost frames
Option to fix latency at configurable value
BTrainFrameTransceiver
API to the user logic (VHDL records)
Encoding/decoding of BTrain Frames (format agreed by all BTrain users)
Transmission/reception of BTrain frames using WR Streamers
Comprehensive documentation and VHDL Reference Designs:
SPEC, SVEC, VFC-HD, VXS, CUTE-DP-WR boards
BTrainFrameTxRx
WR Streamers
WR PTP Core
FIFO
FIFO
Latency
BFrame
IFrame
WR Switch
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home

## Slide 72: Support and monitoring
19
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
Developed by BE-CO-HT, support eventually by TE-MSC-MM
CO-supported
Developed by BE-CO-HT, support eventually by TE-MSC-MM

## Slide 73: Support and monitoring
WR Switch
19
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
Developed by BE-CO-HT, support eventually by TE-MSC-MM
CO-supported
Controls Open Source
MOnitoring System
WR NEtwork MOnitoring
and Configuration
Nodes monitoring
over SNMP
Switch monitoring
over SNMP
Monitoring
WR Switch and its ports state
WR Node state
Frames tx/rx/lost
Max/min/avg latency
Developed by BE-CO-HT, support eventually by TE-MSC-MM

## Slide 74: Support and monitoring
WR Switch
19
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
Developed by BE-CO-HT, support eventually by TE-MSC-MM
CO-supported
Controls Open Source
MOnitoring System
WR NEtwork MOnitoring
and Configuration
Nodes monitoring
over SNMP
Switch monitoring
over SNMP
Monitoring
WR Switch and its ports state
WR Node state
Frames tx/rx/lost
Max/min/avg latency
Developed by BE-CO-HT, support eventually by TE-MSC-MM

## Slide 75: Support and monitoring
WR Switch
19
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
Developed by BE-CO-HT, support eventually by TE-MSC-MM
CO-supported
Controls Open Source
MOnitoring System
WR NEtwork MOnitoring
and Configuration
Nodes monitoring
over SNMP
Switch monitoring
over SNMP
Monitoring
WR Switch and its ports state
WR Node state
Frames tx/rx/lost
Max/min/avg latency
Developed by BE-CO-HT, support eventually by TE-MSC-MM

## Slide 76: Support and monitoring
WR Switch
19
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
Developed by BE-CO-HT, support eventually by TE-MSC-MM
CO-supported
Controls Open Source
MOnitoring System
WR NEtwork MOnitoring
and Configuration
Nodes monitoring
over SNMP
Switch monitoring
over SNMP
Monitoring
WR Switch and its ports state
WR Node state
Frames tx/rx/lost
Max/min/avg latency
Developed by BE-CO-HT, support eventually by TE-MSC-MM

## Slide 77: Status and Plans for BTrain over White Rabbit
20
Before LS2, successfully used in operation
  PS: since 2015
  ELENA: since its start – no legacy BTrain
  PSB / LEIR: at the end of run 2
with the above features included

## Slide 78: Status and Plans for BTrain over White Rabbit
20
Before LS2, successfully used in operation
  PS: since 2015
  ELENA: since its start – no legacy BTrain
  PSB / LEIR: at the end of run 2
During LS2
  Release v1.2 of BTrain over WhiteRabbit : (https://gitlab.cern.ch/BTrain-Team/BTrain-over-WhiteRabbit/-/wikis/releases)
    WR streamers fixed-latency improved from ± 8ns to sub-ns
    Support for Cute-WR-DP FMC
    Support for BTrain API on FMC pins
  Deployment of WR Nodes monitoring
  Update of WR Switch firmware/config
FMC card
FMC carrier

## Slide 79: Status and Plans for BTrain over White Rabbit
20
Before LS2, successfully used in operation
  PS: since 2015
  ELENA: since its start – no legacy BTrain
  PSB / LEIR: at the end of run 2
During LS2
  Release v1.2 of BTrain over WhiteRabbit : (https://gitlab.cern.ch/BTrain-Team/BTrain-over-WhiteRabbit/-/wikis/releases)
    WR streamers fixed-latency improved from ± 8ns to sub-ns
    Support for Cute-WR-DP FMC
    Support for BTrain API on FMC pins
  Deployment of WR Nodes monitoring
  Update of WR Switch firmware/config
After LS2, operational in PSB, LEIR, PS, SPS, AD, ELENA
FMC card
FMC carrier

## Slide 80: Conclusions
21
BTrain – critical system in PSB, LEIR, PS, SPS, AD, ELENA
White Rabbit – suitable CO-supported technology, versatile and flexible
BTrain over White Rabbit
  at the heart of the FIRESTORM project
  common interface between all BTrain users
  a smooth inter-department and inter-group collaboration between TE-MSC, TE-EPC, BE-RF, BE-BI facilitated BE-CO.
See: https://wikis.cern.ch/display/HT/Btrain+over+White+Rabbit

## Slide 81: Conclusions
21
BTrain – critical system in PSB, LEIR, PS, SPS, AD, ELENA
White Rabbit – suitable CO-supported technology, versatile and flexible
BTrain over White Rabbit
  at the heart of the FIRESTORM project
  common interface between all BTrain users
  a smooth inter-department and inter-group collaboration between TE-MSC, TE-EPC, BE-RF, BE-BI facilitated BE-CO.
See: https://wikis.cern.ch/display/HT/Btrain+over+White+Rabbit
Thank you !

## Slide 82: Outline
Introduction to WR and overview of its applications
BTrain over WR (Maciej)
WR Trigger Distribution (Dimitris)
RF Signal Distribution over WR (John)
Q&A