## Slide 1: White Rabbit Applications
John Gill, Dimitris Lampridis, Maciej Lipinski
CERN BE-CO
Hardware and Timing Section
BE Seminar
22 November 2019

## Slide 2: Outline
WR in a nutshell
BTrain over WR (Maciej)
WR Trigger Distribution (Dimitris)
RF Signal Distribution over WR (John)
Q&A
2

## Slide 3: Outline
WR in a nutshell
BTrain over WR (Maciej)
WR Trigger Distribution (Dimitris)
RF Signal Distribution over WR (John)
Q&A
2

## Slide 4: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing

## Slide 5: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)

## Slide 6: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)

## Slide 7: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)

## Slide 8: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation (included in IEEE 1588)
  Deterministic data transfer

## Slide 9: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation (included in IEEE 1588)
  Deterministic data transfer
Initial specs: links ≤10 km & ≤2000 nodes

## Slide 10: White Rabbit in a nutshell
3
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation (included in IEEE 1588)
  Deterministic data transfer
Initial specs: links ≤10 km & ≤2000 nodes
Open Source and commercially available

## Slide 11: White Rabbit in a nutshell
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation (included in IEEE 1588)
  Deterministic data transfer
Initial specs: links ≤10 km & ≤2000 nodes
Open Source and commercially available
Many applications worldwide
3
Large High Altitude Air
Shower Observatory
German Stock Exchange
National Time Labs
(NL, FI, FR, US, UK, IT)
CERN & GSI
Accelerator Facilities
Cubic Kilometre
Neutrino Telescope
European Space Agency
for Galileo
Telecommunication for High Accuracy Time Dissemination
http://www.ohwr.org/projects/white-rabbit/wiki/WRUsers

## Slide 12: White Rabbit in a nutshell
CERN and GSI initiative for control & timing
Based on well-established standards
  Ethernet (IEEE 802.3)
  Bridged Local Area Network (IEEE 802.1Q)
  Precision Time Protocol (IEEE 1588)
Extends standards to provide
  Sub-ns synchronisation (included in IEEE 1588)
  Deterministic data transfer
Initial specs: links ≤10 km & ≤2000 nodes
Open Source and commercially available
Many applications worldwide
More in “Introduction to WR Technologies” https://indico.cern.ch/event/862562/
3
Large High Altitude Air
Shower Observatory
German Stock Exchange
National Time Labs
(NL, FI, FR, US, UK, IT)
CERN & GSI
Accelerator Facilities
Cubic Kilometre
Neutrino Telescope
European Space Agency
for Galileo
Telecommunication for High Accuracy Time Dissemination
http://www.ohwr.org/projects/white-rabbit/wiki/WRUsers

## Slide 13: Outline
WR in a nutshell
BTrain over WR (Maciej)
WR Trigger Distribution (Dimitris)
RF Signal Distribution over WR (John)
Q&A

## Slide 14: Synchrotron operation
4
Beam Inst.
Diagnostics
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Coordination required between:
f (t) – RF in accelerating cavities
B(t) – magnetic field in bending magnets
I(t) – current provided by power converters
Beam Instrumentation diagnostics
I(t)

## Slide 15: Synchrotron operation
4
Beam Inst.
Diagnostics
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Coordination required between:
f (t) – RF in accelerating cavities
B(t) – magnetic field in bending magnets
I(t) – current provided by power converters
Beam Instrumentation diagnostics
Coordination provided by
the BTrain system
I(t)

## Slide 16: BTrain System
5
Beam Inst.
Diagnostics
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
I(t)

## Slide 17: BTrain System
5
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
B
B
B
Beam Inst.
Diagnostics
I(t)

## Slide 18: BTrain System
5
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
B
B
B
Beam Inst.
Diagnostics
I(t)
1us
24V
0.1 Gauss =
(max 500kHz)

## Slide 19: BTrain System
5
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Bflat top
time
B(t)
Bflat bottom
t1
t2
Peaking strip
marker 1
marker 2 (optional)
coil measurement Vcoil ~ Ḃ
B
B
B
Beam Inst.
Diagnostics
I(t)

## Slide 20: BTrain System
5
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Bflat top
time
B(t)
Bflat bottom
t1
t2
Peaking strip
marker 1
marker 2 (optional)
coil measurement Vcoil ~ Ḃ
+0.1G
- 0.1G
preset B(t1)
B(t)
B
B
B
Beam Inst.
Diagnostics
I(t)

## Slide 21: BTrain System
5
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Bflat top
time
B(t)
Bflat bottom
t1
t2
Peaking strip
marker 1
marker 2 (optional)
coil measurement Vcoil ~ Ḃ
+0.1G
- 0.1G
preset B(t1)
B(t)
B
B
B
Beam Inst.
Diagnostics
~ Vcoil
I(t)

## Slide 22: FIRESTORM to renovate BTrain
6
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Project by Magnets, Superconductors & Cryostats (TE-MSC) Group in collaboration with TE-EPC, BE-RF, BE-BI & BE-CO.
Why to renovate:
Higher resolution (0.05G) required in PS
Peak slope of 6T/s required by PSB
Spikes & noise on Bdot, timing problems with marker
Obsolete measurement technology and aging components
Non-standard equipment, little support from CO
Not uniform across accelerators & limited diagnostics
What to renovate:
Measurement technology – new markers and coils
Data transfer technology – White Rabbit
B
B
B
Beam Inst.
Diagnostics
I(t)

## Slide 23: FIRESTORM to renovate BTrain
6
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
Project by Magnets, Superconductors & Cryostats (TE-MSC) Group in collaboration with TE-EPC, BE-RF, BE-BI & BE-CO.
Why to renovate:
Higher resolution (0.05G) required in PS
Peak slope of 6T/s required by PSB
Spikes & noise on Bdot, timing problems with marker
Obsolete measurement technology and aging components
Non-standard equipment, little support from CO
Not uniform across accelerators & limited diagnostics
What to renovate:
Measurement technology – new markers and coils
Data transfer technology – White Rabbit
I(t)
WR Switch
WR Node

## Slide 24: BTrain data transfer over WR
7
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
WR Switch

## Slide 25: BTrain data transfer over WR
7
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
Digitally distributes absolute values of B and Bdot in Ethernet frames
Distributes simultaneously B from different sources (old B, measured B, simulated B, synthesized B)
Provides additional control information (C0, marker)
Supports resolution down to 0.0001G
Allows rates >500kHz and infinitely fast ramps
Deterministic & guarantees max latency of 10us
Provides extensive diagnostics
Provides flexibility and scalability
  I(t) is sent back for model analysis
CTRL | B | Bdot | oldB | meaB | simB | synB
WR Switch
CTRL
I
Payload of Ethernet Frame

## Slide 26: BTrain data transfer over WR
7
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
Digitally distributes absolute values of B and Bdot in Ethernet frames
Distributes simultaneously B from different sources (old B, measured B, simulated B, synthesized B)
Provides additional control information (C0, marker)
Supports resolution down to 0.0001G
Allows rates >500kHz and infinitely fast ramps
Deterministic & guarantees max latency of 10us
Provides extensive diagnostics
Provides flexibility and scalability
  I(t) is sent back for model analysis
  I(t) exchanged internally for Pole Face Winding (PFW) of Power Converters
CTRL | B | Bdot | oldB | meaB | simB | synB
WR Switch
CTRL
I
Payload of Ethernet Frame

## Slide 27: BTrain data transfer over WR
7
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
Digitally distributes absolute values of B and Bdot in Ethernet frames
Distributes simultaneously B from different sources (old B, measured B, simulated B, synthesized B)
Provides additional control information (C0, marker)
Supports resolution down to 0.0001G
Allows rates >500kHz and infinitely fast ramps
Deterministic & guarantees max latency of 10us
Provides extensive diagnostics
Provides flexibility and scalability
  I(t) is sent back for model analysis
  I(t) exchanged internally for Pole Face Winding (PFW) of Power Converters
CTRL | B | Bdot | oldB | meaB | simB | synB
WR Switch
CTRL
I
Payload of Ethernet Frame
SPS RF
  NOTE: Accelerating RF cavities to be
  controlled in SPS using WR

## Slide 28: WR-BTrain Nodes
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
WR Switch
8

## Slide 29: WR-BTrain Nodes
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
WR Switch
8
FPGA
FPGA
FPGA
Simple VME64x FMC Carrier (SVEC)
Simple PCIe FMC carrier (SPEC)
VME FMC Carrier HPC-DDR3 (VFC-HD)
VXS Switch
FPGA

## Slide 30: WR-BTrain Nodes
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
WR Switch
8
CO-supported
hardware
FPGA
FPGA
FPGA
FPGA
Simple VME64x FMC Carrier (SVEC)
Simple PCIe FMC carrier (SPEC)
VME FMC Carrier HPC-DDR3 (VFC-HD)
VXS Switch

## Slide 31: WR-BTrain Nodes
FPGA
V
Power
converter
B (t)
frev (t)
Accelerating
RF cavity
Bending
magnet
Beam Inst.
Diagnostics
I(t)
Simple VME64x FMC Carrier (SVEC)
Simple PCIe FMC carrier (SPEC)
VME FMC Carrier HPC-DDR3 (VFC-HD)
VXS Switch
WR Switch
8
FPGA
FPGA
FPGA
CO-support
for
White Rabbit

## Slide 32: BTrain over White Rabbit Project
9
WR Switch
FPGA
BTrain over
White Rabbit
B
I
User logic
FPGA
BTrain over
White Rabbit
B
I
User logic
FPGA
BTrain over
White Rabbit
B
I
User logic
FPGA
BTrain over
White Rabbit
B
I
User logic
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home
FPGA
FPGA
FPGA
Simple VME64x FMC Carrier (SVEC)
Simple PCIe FMC carrier (SPEC)
VME FMC Carrier HPC-DDR3 (VFC-HD)
VXS Switch
FPGA

## Slide 33: BTrain over White Rabbit Project
WR Switch
9
FPGA
BTrain over
White Rabbit
B
I
User logic
FPGA
BTrain over
White Rabbit
B
I
User logic
FPGA
BTrain over
White Rabbit
B
I
User logic
FPGA
BTrain over
White Rabbit
B
I
User logic
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home

## Slide 34: BTrain over White Rabbit Project
WR Switch
9
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
FPGA
B
I
User logic
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network
WR Streamers
Data Transfer Layer: FIFO over White Rabbit
Statistics of network latency and lost frames
Option to fix latency at configurable value
BTrainFrameTransceiver
API to the user logic (VHDL records)
Encoding/decoding of BTrain Frames (format agreed by all BTrain users)
Transmission/reception of BTrain frames using WR Streamers
BTrainFrameTxRx
WR Streamers
WR PTP Core
BTrainFrameTxRx
WR Streamers
WR PTP Core
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home

## Slide 35: BTrain over White Rabbit Project
9
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network
WR Streamers
Data Transfer Layer: FIFO over White Rabbit
Statistics of network latency and lost frames
Option to fix latency at configurable value
BTrainFrameTransceiver
API to the user logic (VHDL records)
Encoding/decoding of BTrain Frames (format agreed by all BTrain users)
Transmission/reception of BTrain frames using WR Streamers
BTrainFrameTxRx
WR Streamers
WR PTP Core
WR Switch
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home

## Slide 36: BTrain over White Rabbit Project
WR Switch
9
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network

## Slide 37: BTrain over White Rabbit Project
9
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FIFO
FIFO
Latency
word
word
WR Switch
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network
WR Streamers
Data Transfer Layer: FIFO over White Rabbit
Statistics of network latency and lost frames
Option to fix latency at configurable value

## Slide 38: BTrain over White Rabbit Project
9
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FIFO
FIFO
Latency
word
word
WR Switch
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network
WR Streamers
Data Transfer Layer: FIFO over White Rabbit
Statistics of network latency and lost frames
Option to fix latency at configurable value

## Slide 39: BTrain over White Rabbit Project
9
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FIFO
FIFO
Latency
BFrame
IFrame
WR Switch
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network
WR Streamers
Data Transfer Layer: FIFO over White Rabbit
Statistics of network latency and lost frames
Option to fix latency at configurable value
BTrainFrameTransceiver
API to the user logic (VHDL records)
Encoding/decoding of BTrain Frames (format agreed by all BTrain users)
Transmission/reception of BTrain frames using WR Streamers

## Slide 40: BTrain over White Rabbit Project
9
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
WR PTP Core
WR time and Ethernet Frames
Diagnostics over WR network
WR Streamers
Data Transfer Layer: FIFO over White Rabbit
Statistics of network latency and lost frames
Option to fix latency at configurable value
BTrainFrameTransceiver
API to the user logic (VHDL records)
Encoding/decoding of BTrain Frames (format agreed by all BTrain users)
Transmission/reception of BTrain frames using WR Streamers
Comprehensive documentation and VHDL Reference Designs:
SPEC, SVEC, VFC-HD, VXS boards
BTrainFrameTxRx
WR Streamers
WR PTP Core
FIFO
FIFO
Latency
BFrame
IFrame
WR Switch
https://gitlab.cern.ch/BTrain-TEAM/Btrain-over-WhiteRabbit/wikis/home

## Slide 41: Support and monitoring
10
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
Developed by BE-CO-HT, support eventually by TE-MSC-MM
CO-supported
Developed by BE-CO-HT, support eventually by TE-MSC-MM

## Slide 42: Support and monitoring
WR Switch
10
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
Developed by BE-CO-HT, support eventually by TE-MSC-MM
CO-supported
Controls Open Source
MOnitoring System
WR NEtwork MOnitoring
and Configuration
Nodes monitoring
over SNMP
Switch monitoring
over SNMP
Monitoring
WR Switch and its ports state
WR Node state
Frames tx/rx/lost
Max/min/avg latency
Developed by BE-CO-HT, support eventually by TE-MSC-MM

## Slide 43: Support and monitoring
WR Switch
10
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
Developed by BE-CO-HT, support eventually by TE-MSC-MM
CO-supported
Controls Open Source
MOnitoring System
WR NEtwork MOnitoring
and Configuration
Nodes monitoring
over SNMP
Switch monitoring
over SNMP
Monitoring
WR Switch and its ports state
WR Node state
Frames tx/rx/lost
Max/min/avg latency
Developed by BE-CO-HT, support eventually by TE-MSC-MM

## Slide 44: Support and monitoring
WR Switch
10
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
FPGA
B
I
User logic
BTrainFrameTxRx
WR Streamers
WR PTP Core
Developed by BE-CO-HT, support eventually by TE-MSC-MM
CO-supported
Controls Open Source
MOnitoring System
WR NEtwork MOnitoring
and Configuration
Nodes monitoring
over SNMP
Switch monitoring
over SNMP
Monitoring
WR Switch and its ports state
WR Node state
Frames tx/rx/lost
Max/min/avg latency
Developed by BE-CO-HT, support eventually by TE-MSC-MM

## Slide 45: Status and Plans for BTrain over White Rabbit
11
Before LS2, successfully used in operation
  PS: since 2015
  ELENA: since its start – no legacy BTrain
  PSB / LEIR: at the end of run 2
After LS2, operational in PSB, LEIR, PS, SPS, AD, ELENA
with the above features included

## Slide 46: Status and Plans for BTrain over White Rabbit
11
Before LS2, successfully used in operation
  PS: since 2015
  ELENA: since its start – no legacy BTrain
  PSB / LEIR: at the end of run 2
After LS2, operational in PSB, LEIR, PS, SPS, AD, ELENA
Ongoing work – to be included in next release of BTrain over WhiteRabbit :
  WR streamers fixed-latency improved from ± 8ns to sub-ns
  Support for Cute-WR-DP FMC
  Support for user API on FMC pins
FMC card
FMC carrier

## Slide 47: Conclusions
12
BTrain – critical system in PSB, LEIR, PS, SPS, AD, ELENA
White Rabbit – suitable CO-supported technology, versatile and flexible
BTrain over White Rabbit
  at the heart of the FIRESTORM project
  common interface between all BTrain users
  a smooth inter-departament and inter-group collaboration between TE-MSC, TE-EPC, BE-RF, BE-BI facilitated BE-CO.
See: https://wikis.cern.ch/display/HT/Btrain+over+White+Rabbit

## Slide 48: Conclusions
12
BTrain – critical system in PSB, LEIR, PS, SPS, AD, ELENA
White Rabbit – suitable CO-supported technology, versatile and flexible
BTrain over White Rabbit
  at the heart of the FIRESTORM project
  common interface between all BTrain users
  a smooth inter-departament and inter-group collaboration between TE-MSC, TE-EPC, BE-RF, BE-BI facilitated BE-CO.
See: https://wikis.cern.ch/display/HT/Btrain+over+White+Rabbit
Thank you !

## Slide 49: Outline
WR in a nutshell
BTrain over WR (Maciej)
WR Trigger Distribution (Dimitris)
RF Signal Distribution over WR (John)
Q&A

## Slide 50: Backup slides

## Slide 51: BTrain over WR network and its configuration
See: https://wikis.cern.ch/display/HT/Btrain+over+White+Rabbit
The same architecture/config for all accelerators
Two redundant control chains: operational and spare
VLANs used extensively to enforce proper flow of information