## Slide 1: White Rabbit standardization in IEEE1588-20XX
Maciej Lipinski
(based on Greg’s presentation)

## Slide 2: IEEE standard lifecycle
Maintaining the standard
Initiating the project
Mobilizing the working group
Drafting the standard
Balloting the standard
Gaining final approval

## Slide 3: IEEE1588 standard revision
Currently: IEEE1588-2008
Revision started in June 2013
Enforced by standard life-cycle

## Slide 4: IEEE1588 standard revision
Currently: IEEE1588-2008
Revision started in June 2013
Enforced by standard life-cycle
Performed by P1588 Working Group with over 200 members
Divided into 5 sub-committees

## Slide 5: IEEE1588 standard revision
Currently: IEEE1588-2008
Revision started in June 2013
Enforced by standard life-cycle
Performed by P1588 Working Group with over 200 members
Divided into 5 sub-committees
High Accuracy (HA) sub-committee dedicated to White Rabbit

## Slide 6: White Rabbit split into 5 parts
L1 syntonization
Delay asymmetry estimation and correction of PTP calculations for delay asymmetry and hardware delays
Calibration procedure
Assignment of fixed roles (master/slave) to WR ports
WR PTP profile compatible with Delay Request-Response default PTP profile

## Slide 7: 1. L1 syntonization in WR
Local PTP clock is the same as L1 clock

## Slide 8: 1. L1 syntonization in HA
Flexible and configurable relation between PTP and L1 clocks
All phase offsets known and pseudo-constant

## Slide 9: 1. L1 syntonization in HA
Introduces a new L1 state machine
Semi-independent from PTP state machine
Detects if a peer port supports L1Sync
Handles L1 configuration matching

## Slide 10: 2. Correction of PTP calculations
Delay asymmetry estimation:
  In WR:
  In HA:

## Slide 11: 2. Correction of PTP calculations
Delay asymmetry estimation:
  In WR:
  In HA:
Hardware delays:
  In WR: only Slave corrects for
  In HA: both Master and Slave correct timestamps for ingress/egress latencies

## Slide 12: 3. WR Calibration procedure v1.1
In HA: “Calibration Procedures”
Rewritten into informative annex
Rewritten to use IEEE-1588 terminology and data sets
Exactly the same step-by-step procedure
Does not include
  Mathematical proofs
  Measurement errors estimation
Notes: MasterOnly PTP ports – BMC running, but some ports disalowed from being Slave
External configuration – disable BMCA, use management to configure port state

## Slide 13: 4. Assignment of fixed roles
MasterOnly PTP Ports
  Best Master Clock Algorithm running
  Some ports disallowed from becoming PTP Slaves
Notes: MasterOnly PTP ports – BMC running, but some ports disalowed from being Slave
External configuration – disable BMCA, use management to configure port state

## Slide 14: 4. Assignment of fixed roles
MasterOnly PTP Ports
  Best Master Clock Algorithm running
  Some ports disallowed from becoming PTP Slaves
Mechanism for external role configuration
  Best Master Clock Algorithm disabled
  External mechanism to configure PTP port state
Notes: MasterOnly PTP ports – BMC running, but some ports disalowed from being Slave
External configuration – disable BMCA, use management to configure port state

## Slide 15: 5. WR PTP Profile
“High Accuracy Delay Request-Response Default PTP Profile”
Extends Delay Req-Resp Default PTP Profile
Mandates support of optional features required by High Accuracy
Defines default and allowed values for the optional features
Interoperates with Delay Req-Resp Default Profile
Defines High Accuracy Clock Model
  Syntonization through Layer-1
  Synchronization through PTP
Notes: MasterOnly PTP ports – BMC running, but some ports disalowed from being Slave
External configuration – disable BMCA, use management to configure port state

## Slide 16: Where is WR in IEEE1588-20XX?
L1 syntonization – Annex O
Correction of PTP calculations – Clause 16.7 / 16.8
Calibration procedure – Annex Q
Assignment of fixed roles – Clause 9.2.2.2 / 8.2.15.5.2 / 17.6
HA PTP Profile – Annex J.5
Sub-ns implementation – Annex P
Changes to core parts of the standard: https://www.ohwr.org/projects/wr-std/wiki/wrin1588

## Slide 17: Where is WR in IEEE1588-20XX?
Generic optional features
HA-specific optional features
L1 Sync
Configurable correction of timestamps
High Accuracy Default PTP Profile
(Addition to Annex J)
Sub-ns synchronization using High Accuracy Default Profile
(Annex P)
HA Profile uses and requires support of
the HA and other optional features
Informative annex describes HA Profile
implementation that provides
sub-ns accuracy of synchronization
Changes to the main clause of IEEE1588
HA features require changes to 1588 clauses
Mechanism for external configuration
master Only
mode
Calculation of the delayAsymmetry

## Slide 18: IEEE1588-20XX standardization process
Project Authorization Request (PAR)
2013 Jun: start

## Slide 19: IEEE1588-20XX standardization process
2013 Jun: start
2016 Jan: stop new ideas
2016 Dec: PTP draft ready / 1st Ballot starts

## Slide 20: IEEE1588-20XX standardization process
2013 Jun: start
2016 Jan: stop new ideas
2016 Dec: PTP draft ready / 1st Ballot starts
2017 Nov: 2nd Ballot starts
2018 Feb: 3rd Ballot starts

## Slide 21: IEEE1588-20XX standardization process
2013 Jun: start
2016 Jan: stop new ideas
2016 Dec: PTP draft ready / 1st Ballot starts
2017 Nov: 2nd Ballot starts
2018 Feb: 3rd Ballot starts
2018 Aug: Sponsor Ballot

## Slide 22: IEEE1588-20XX standardization process
2013 Jun: start
2016 Jan: stop new ideas
2016 Dec: PTP draft ready / 1st Ballot starts
2017 Nov: 2nd Ballot starts
2018 Feb: 3rd Ballot starts
2018 Aug: Sponsor Ballot
2019 Mid: Final draft ready

## Slide 23: IEEE1588-20XX standardization process
2013 Jun: start
2016 Jan: stop new ideas
2016 Dec: PTP draft ready / 1st Ballot starts
2017 Nov: 2nd Ballot starts
2018 Feb: 3rd Ballot starts
2018 Aug: Sponsor Ballot
2019 Mid: Final draft ready
End-2019: Publication

## Slide 24: IEEE1588-HA implementation
2013 Jun: start
2016 Jan: stop new ideas
2016 Dec: PTP draft ready /
1st Ballot starts
2017 Nov: 2nd Ballot starts
2018 Feb: 3rd Ballot starts
2018 Aug: Sponsor Ballot
2019 Mid: Final draft ready
End-2019: Publication
2016 Sep: First implementation of L1 sync

## Slide 25: IEEE1588-HA implementation
2013 Jun: start
2016 Jan: stop new ideas
2016 Dec: PTP draft ready /
1st Ballot starts
2017 Nov: 2nd Ballot starts
2018 Feb: 3rd Ballot starts
2018 Aug: Sponsor Ballot
2019 Mid: Final draft ready
End-2019: Publication
2016 Sep: Prototype implementation of L1 sync
now:
Automated compliance tests by Veryx
Ongoing work on HA implementation
HA demonstrated on ISPCS2018

## Slide 26: Summary
White Rabbit becomes High Accuracy profile of IEEE1588-20XX
New release of standard in final stage of preparation
Now going through the first Sponsor Balloting phase
We’re working on first HA implementation
Compliance tests developed independently
New IEEE-1588 standard to be published (hopefully) in 2019